## Slide 1: CISP 310 Assembly Language Programming for Microcomputers
Fall 2016
Professor Suha Aljuboori
Lecture1

## Slide 2: Chapter One Representing Data in Computer

## Slide 3: Data Representation
Data refers to the symbols that represent people, events, things, and ideas. Data can be a name, a number, the colors in a photograph, or the notes in a musical composition.
Numeric or Character Data
Data representation refers to the form in which data is stored, processed, and transmitted.
Binary digit (Bit) 0,1

## Slide 4: Memory Conventions

## Slide 5
Why Kilo=1024 not 1000
It’s all because binary numbers are of Base 2
Base 2 | Decimal
 | 1
 | 2
 | 4
 | 8
 | 16
 | 32
 | 64
 | 128
 | 256
 | 512
 | 1,024
Base 2 | Decimal
 | 1
 | 2
 | 4
 | 8
 | 16
 | 32
 | 64
 | 128
 | 256
 | 512
 | 1,024

## Slide 6
Base 2: Binary
Base 8: Octal
Base 10: Decimal
Base 16: Hexadecimal
Numbering Systems

## Slide 7: Binary
Numbers representing using 0 , 1
It’s the decimal system except that the positions (right to left) are:
1’s, 2’s, 4’s, 8’s, 16’s (and higher powers of 2)
instead of 1’s, 10’s, 100’s, 1000’s, 10000’s (powers of 10)
Example:
The Binary number 0110 = 6 in Decimal

## Slide 8: Conversion
Decimal to Binary
  Division Method
  Subtraction Method
Binary to Decimal
  Multiplication Method
  Addition Method
Both
  Easy Method

## Slide 9: Division Method
35 ÷ 2 = 17 Remainder 1
17 ÷ 2 = 8 Remainder 1
8 ÷ 2 = 4 Remainder 0
4 ÷ 2 = 2 Remainder 0
2 ÷ 2 = 1 Remainder 0
1 ÷ 2 = 0 Remainder 1
Bottom Up
100011 = 35

## Slide 10: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 |  |  |  |  |  |  |  |  |  | 

## Slide 11: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 |  |  |  |  |  |  |  |  | 

## Slide 12: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 |  |  |  |  |  |  |  | 

## Slide 13: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 |  |  |  |  |  |  | 
227 - 128 = 99

## Slide 14: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 1 |  |  |  |  |  | 
227 - 128 = 99
99 – 64 = 35

## Slide 15: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 1 | 1 |  |  |  |  | 
227 - 128 = 99
99 – 64 = 35
35 - 32 = 3

## Slide 16: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 1 | 1 | 0 |  |  |  | 
227 - 128 = 99
99 – 64 = 35
35 - 32 = 3

## Slide 17: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 |  |  | 
227 - 128 = 99
99 – 64 = 35
35 - 32 = 3

## Slide 18: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 |  | 
227 - 128 = 99
99 – 64 = 35
35 - 32 = 3

## Slide 19: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 
227 - 128 = 99
99 – 64 = 35
35 - 32 = 3
3 - 2 = 1

## Slide 20: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
227 - 128 = 99
99 – 64 = 35
35 - 32 = 3
3 - 2 = 1
1 - 1 = 0

## Slide 21: Subtraction Method
Convert 227 to binary:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
227 - 128 = 99
99 – 64 = 35
35 - 32 = 3
3 - 2 = 1
1 - 1 = 0
227 = 1110 0011

## Slide 22: Multiplication Method
Repeated multiplication by 2
Convert 1100 to decimal:
1100b = 12d
0 * 2 + 1 = 1
1 * 2 + 1 = 3
3 * 2 + 0 = 6
6 * 2 + 0 = 12
Notes: This is the best long-hand method. You can use this to convert to any base, and all you have to remember in your head is the running tally.

## Slide 23: Addition Method
Convert 0100 0001 0011 to decimal:
2^10 | 2^9 | 2^8 | 2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1
1024 + 0 + 0 + 0 + 0 + 0 + 16 + 0 + 0 + 2 + 1 = 1043
0100 0001 0011b = 1043d

## Slide 24: Easy Method

## Slide 25: Octal
In Octal, a binary number is divided up into groups of only 3 bits
Each group or set of bits having a distinct value of between 000 (0) and 111 ( 4+2+1 = 7 ).
Counting in Octal
  1 2 3 4 5 6 7 10 11 12 13 14 15 17 20

## Slide 26: Octal Decimal Binary
Octal | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 10 | 11 | 12
Decimal | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Binary | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111 | 001 000 | 001 001 | 001

## Slide 27: Hexadecimal
The hexadecimal (base 16) number system represents numbers using about one fourth as many digits as the binary system.

## Slide 28: Counting with hexadecimal
0 1 2 3 4 5 6 7 8 9 A B C D E F 10
11 12 13 14 15 16 17 18 19 1A 1B 1C 1D 1E 1F 20

## Slide 29: Conversion: To convert from hex to binary
Substitute 4 bits for each hex digit
3B8E2 = 11 1011 1000 1110 0010
To convert binary to hex
Break the binary number into groups of 4 bits, starting from the right, and substitute the corresponding hex digit for each group of 4 bits
1011011101001101111 = 101|1011|1010|0110|1111 = 5BA6F

## Slide 30: Conversion: To convert from hex to decimal
The positions in hexadecimal numbers correspond to powers of 16. From right to left, they are 1’s, 16’s, 256’s, and so on.
Convert the hex number 6BD3 to decimal
6 * 4096 = 24576 ( 4096 = )
+ 11 * 256 = 2816 ( B is 11 , 256 = )
+ 13 * 16 = 208 ( D is 13 )
+ 3 * 1 = 3
= 27603

## Slide 31: To convert from decimal to hex
Using repeated division by 16
Convert the decimal number 855 to hex
855 ÷ 16 = 53 Reminder 7
53 ÷ 16 = 3 Reminder 5
3 ÷ 16 = 0 Reminder 3
Result in hex = 357

## Slide 32: Representing Charcters
The system commonly used with microcomputers is the American Standard Code for Information Interchange (ASCII).
The ASCII code uses 7 bit to represent characters
For example

## Slide 34: Signe and Unsigned Representation
Standard Number Lengths
Byte – 8 bits
Word – 16 bits
Doubleword – 32 bits
Quadword – 64 bits

## Slide 35: Examples:
Give us the word length binary representation of the decimal number 335
Binary =101001111, Word-length binary= 0000000101001111
Give us the word length hex representation of the decimal number 335
hex =14F , Word-length hex= 014F
01 | 4F

## Slide 36: Unsigned Representation
Just binary in one of the standard lengths
16D9 is the word-length unsigned representation for the decimal number 5849.

## Slide 37: Signed Representation
Signed Magnitude
leftmost digit used as a sign indication, if it’s 0 the number is positive, if it’s 1 the number is negative.
00001010 = decimal 10
10001010 = decimal -10
2’s complement representation
Use One of tthe sandard lengths
High-order (leading) bit gives sign
  0 for positive
  1 for negative
for example, that the most positive number that can be represented in word-size 2’s complement form is 01111111111111112 or 7FFF16 or 3276710.
For a negative number, you must perform the 2’s complement operation to find the corresponding positive number.

## Slide 38: 2’s Complement Operation in Hex
+/- button on many calculators
Manually by subtracting from 100…0
Example:
E47A represents a negative word-length signed number since E = 1110
10000 – E47A = 1B86 = 704610, so E47A is the 2’s complement signed representation for –7046

## Slide 39: 2’s Complement Operation in Binary
The Two’s Complement of a binary number is basically another number which, when added to the original, will make all bits become zeroes.
Steps:
  Find the one’s complement
  add 1 to it.
Example
  The binary representation of 12 is 00001100.
  It’s one’s complement is 11110011.
  Add one to that and we have its two’s complement.
  11110011 (one's complement of 12) + 00000001 (decimal 1) = 11110100 (two's complement of 12)

## Slide 40: 1’s Complement Operation
1’s complement negate a number by fliping3 all its bits.
The 1’s complement of 01110000 is 10001111.
1’s complement rarely used for signed integers in modern systems

## Slide 41: Addition and Subtraction

## Slide 42: Binary Addition and Subtraction
Addition
The four basic rules for binary addition are
0 0 0 | 1 0 1 | 0 1 1 | 1 1 01 |  |  |  |  |  | 

## Slide 43: Carry
If the sum of two numbers is one bit longer than the operand size, the extra 1 is a carry (or carry out).
1 | 1 | 1 |  |  | 1 | 1 |  |  |  |  |  |  | 
 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 |  |  |  |  | 
+ | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 |  |  |  |  | 
carry out
carry in

## Slide 44: Subtraction
In a computer, subtraction a − b of numbers a and b is usually performed by taking the 2’s complement of b and adding the result to a. This corresponds to adding the negation of b
There is a borrow in subtraction – when the second number is larger than the first as unsigned numbers.

## Slide 45: Subtraction Example
 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1
- | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
 |  |  | 1 | 1 | 1 | 1 | 1 | 
 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1
+ | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1
 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0

## Slide 46: Multiple Interpretations
One pattern of bits can have many different interpretations.
The word FE89 can be interpreted as
  An unsigned number whose decimal value is 65513
  A signed number whose decimal value is –375

## Slide 47: Integer Addition and Subtraction
Addition
Same for unsigned and 2’s complement signed numbers, but the results may be interpreted differently
The two numbers will be byte-size, word-size, doubleword-size, or quadword-size.
Add the bits and store the sum in the same length as the operands, discarding an extra bit (if any).
 | 0 | A | 0 | 7
+ | 0 | 1 | D | 3
 | 0 | B | D | A

## Slide 48: Carry
If the sum of two numbers is one bit longer than the operand size, the extra 1 is a carry (or carry out).
A carry is discarded when storing the result, but we’ll see how the 80x86 CPU records it.
For unsigned numbers, a carry means that the result was too large to be stored – the answer is wrong.

## Slide 49: Carry In
A 1 carried into the high-order (sign, leftmost) bit position during addition is called a carry in.
Byte-length example
1 | 1 | 1 |  |  | 1 | 1 |  |  |  |  |  |  | 
 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 |  |  |  | E | 7
+ | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 |  |  | + | F | 6
1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 |  |  | 1 | D | D
carry out
carry in

## Slide 50: Overflow
Overflow occurs when there is a carry in but no carry out, or when there is a carry out but no carry in. It recorded by the CPU.
If overflow occurs when adding two signed numbers, then the result will be incorrect.
Word-length example
  Overflow, so AC99 incorrect if viewed as sum of signed numbers
  No carry, so AC99 correct if viewed as sum of unsigned numbers
483F
+ 645A
AC99

## Slide 51: Overflow
If there is no carry in and no carry out, or when there is a carry in but no carry out, then no overflow.

## Slide 52: Overflow
Overflow occurs when there is a carry in but no carry out, or when there is a carry out but no carry in. It recorded by the CPU.
If overflow occurs when adding two signed numbers, then the result will be incorrect.

## Slide 53: Subtraction
If we want to do the following subtraction
Take the 2’s complement of second number and add it to the first number.
CF is set for a borrow in subtraction
 | 0 | 0 | C | 3
+ | F | D | 9 | 6
 | F | E | 5 | 9

## Slide 54
Overflow occurs in subtraction if it occurs in the corresponding addition.
There is a borrow in subtraction – when the second number is larger than the first as unsigned numbers. There is a borrow in subtraction when there is not a carry in the corresponding addition.

## Slide 55: Other Systems For Representing Numbers

## Slide 56: Binary Coded Decimal
BCD uses four bits to encode each decimal digit.
479 could be encoded in two bytes as 0000 0100 0111 1001
The Intel architecture has only a few instructions to do arithmetic on BCD numbers.

## Slide 57: Floating Point
Floating point representation systems allow for nonintegers to be represented, or at least closely approximated.
IEEE single precision is a popular 32-bit format
  Write the number in base 2 “scientific notation”
  Sign bit (0 positive, 1 negative)
  8 bits for exponent (actual exponent plus a bias of 127)
  23 bits for fraction (omitting the leading 1)

## Slide 58: Floating Point Example
78.37510 = 1001110.0112
78 = 1001110
.375 = .o11
In binary, the positions to the right of the binary point 2 (1/2=0.5, ¼=0.25, 1/8=o.125, etc.),

## Slide 59
Convert 11.101 to Decimal
Integral Part = 11B
1*2 + 1*1 =3
Hence, 11B = 3 D
Therefore, 11.101 B = 3.625 D
Fractional Part = .101 B
=1/2 + 0/4 + 1/8
= .625 D